## Slide 1: Sensitivity Analysis and Model Evaluation of Bifenthrin Surface Water Concentrations from California Urban Runoff
Emma Chelsviga, Frederick Ayivia, Yuzhou Luob, Debra Dentonc, Ann Pitchfordd, Sandy Raimondoe, Donald Eberte, S. Thomas Puruckere, Yongping Yuane
aOak Ridge Institute of Science and Engineering (Chelsvig.Emma@epa.gov, frederickayivi@gmail.com)
bCalifornia Department of Pesticide Regulation (Yuzhou.Luo@cdpr.ca.gov)
cU.S. Environmental Protection Agency Region 9 (Denton.Debra@epa.gov)
dRetiree, previously U.S. Environmental Protection Agency, Office of Research and Development (pitchford3@cox.net)
eU.S. Environmental Protection Agency, Office of Research and Development (Raimondo.Sandy@epa.gov, Ebert.Donald@epa.gov, Purucker.Tom@epa.gov, Yuan.Yongping@epa.gov)

## Slide 2: Goals
Employ deterministic and probabilistic approaches with PWC to simulate bifenthrin concentration in runoff
Identify sensitive inputs with respect to model output variability

## Slide 3: Study Overview
Sacramento-San Joaquin River Delta
  Habitat for fish and invertebrate species
  Experiencing habitat loss due to pyrethroid use and its associated pollution
Bifenthrin
  Pyrethroid; toxic to Delta species
  Used by professional pest control applicators for landscape application or as perimeter treatments to structures
  Considerable amount in urban runoff after rain events
Use exposure models (ex., PWC)
Rain

## Slide 4: Site Overview
Storm Drain Locations in Folsom, Sacramento County
Storm Drain Locations in Roseville, Placer County

## Slide 6: PWC
US EPA Office of Pesticide Program
Simulates pesticide concentration in surface water
  Pesticide Root Zone Model (PRZM)
  Variable Volume Water Model (VVWM)
Site-specific inputs
PRZM
VVWM

## Slide 7: Deterministic Model setup
Single value (conservative estimate) for all input parameters
*.wea weather file (Fry et al., 2016)
  One weather station assigned to each storm drain site based on nearest distance between storm drain and grid centroid
  2008 – 2014
PUR monthly application rates
  2009 - 2014
  Bifenthrin application sites included: landscape maintenance, structural pest control, regulatory pest control, rights-of-ways, public health pest control
  Divided monthly urban applications (kg) by urban area in county (ha)
  Homeowner use: Multiplied monthly app rates by 25%, and added this additional amount to monthly rates
  Assumed the amount of pesticide used every day is constant (Gorgoglione et al., 2018)
    Input daily application rates

## Slide 8
Conduct Latin Hypercube sampling for each parameter
Create input data frame and store inputs (5000 values for each parameter)
02_lhs_parameterization.R
lhs_input_ranges.csv
03_write_update_run_pwc.R
04_write_update_vvwm.R
PRZM5.inp
update
PRZM5.exe
*.wea
copy
run PRZM
*.zts
*.prn
vvwmTransfer.txt
VVWM.exe
*.csv
*.txt
copy
run VVWM
update
Create time array
Store outputs as time series (*.RData, *.csv))
Compute PCC (daily and max)
Create PCC graphics
Create percentiles plots
05_write_output_into_df.R
06a_pcc_computation_daily.R
06b_pcc_computation_max.R
07a_pcc_graphics_daily.R
07a2_pcc_graphics_daily.R
07b_pcc_graphics_max.R
07c_percentile_graphics.R
Probabilistic Model setup

## Slide 9: Results
FOL002

## Slide 10: Results
FOL002

## Slide 11: Results
FOL002

## Slide 12: Results
FOL002

## Slide 13: Results

## Slide 14: Results
Sensitivity analysis results (PCC time series plots for sensitive parameters)

## Slide 15: Summary
Summarize findings, etc.

## Slide 16: The End

## Slide 18: Deterministic Input Parameters

## Slide 19: Deterministic Input Parameters

## Slide 20: Deterministic Input Parameters

## Slide 21: Probabilistic Input Ranges

## Slide 22: Probabilistic Input Ranges

## Slide 23: Probabilistic Input Ranges

## Slide 24: Application Rates