## Slide 1: Sensitivity Analysis and Model Evaluation of Bifenthrin Surface Water Concentrations from California Urban Runoff
Emma Chelsviga, Frederick Ayivia, Yuzhou Luob, Debra Dentonc, Ann Pitchfordd, Sandy Raimondoe, Donald Eberte, S. Thomas Puruckere, Yongping Yuane
aOak Ridge Institute of Science and Engineering (Chelsvig.Emma@epa.gov, frederickayivi@gmail.com)
bCalifornia Department of Pesticide Regulation (Yuzhou.Luo@cdpr.ca.gov)
cU.S. Environmental Protection Agency Region 9 (Denton.Debra@epa.gov)
dRetiree, previously U.S. Environmental Protection Agency, Office of Research and Development (pitchford3@cox.net)
eU.S. Environmental Protection Agency, Office of Research and Development (Raimondo.Sandy@epa.gov, Ebert.Donald@epa.gov, Purucker.Tom@epa.gov, Yuan.Yongping@epa.gov)

## Slide 2: Goals
Employ deterministic and probabilistic approaches with PWC to simulate bifenthrin concentration in urban runoff
Identify sensitive inputs with respect to model output variability

## Slide 3: Study Overview
Sacramento-San Joaquin River Delta
  Habitat for fish and invertebrate species
  Experiencing habitat loss due to pyrethroid use and its associated pollution
Bifenthrin
  Pyrethroid; toxic to Delta species
  Used by professional pest control applicators for landscape application or as perimeter treatments to structures
  Considerable amount in urban runoff after rain events
Use exposure models (ex., PWC)
Rain

## Slide 4: PWC
US EPA Office of Pesticide Program
Simulates pesticide concentration in surface water
  Pesticide Root Zone Model (PRZM)
  Variable Volume Waterbody Model (VVWM)
Site-specific inputs
PRZM
VVWM

## Slide 5: Site Overview

## Slide 6
Application Rate Process
PUR Urban Pesticide Use, 2009 – 2014, counties of interest
Sum monthly applications (kg)
Incorporated homeowner use (add 25% of reported urban use)
Luo, 2015 method
  Population fraction of County in Watershed
  Urban Pesticide use in Watershed
Divide application by area of urban land cover in watershed (kg/ha)
Input daily app. rates (2009 – 2014) : divide monthly application rate by number of days in month, and compute a 30-day moving average

## Slide 7: Deterministic Model setup
Single value (conservative estimate) for all input parameters
*.wea weather file (Fry et al., 2016)
  One weather station assigned to each storm drain site based on nearest distance between storm drain and grid centroid
  Precipitation, Evapotranspiration, Temperature, Wind Speed, Solar Radiation
  2008 – 2014
PUR monthly application rates (previous slide)

## Slide 8
Conduct Latin Hypercube sampling for each parameter
Create input data frame and store inputs (5000 values for each parameter)
02_lhs_parameterization.R
lhs_input_ranges.csv
03_write_update_run_pwc.R
04_write_update_vvwm.R
PRZM5.inp
update
PRZM5.exe
*.wea
copy
run PRZM
*.zts
*.prn
vvwmTransfer.txt
VVWM.exe
*.csv
*.txt
copy
run VVWM
update
Create time array
Store outputs as time series (*.RData, *.csv)
Compute PCC (daily and max)
Create PCC graphics
Create percentiles plots
05_write_output_into_df.R
06a_pcc_computation_daily.R
06b_pcc_computation_max.R
07a_pcc_graphics_daily.R
07a2_pcc_graphics_daily.R
07b_pcc_graphics_max.R
07c_percentile_graphics.R
Probabilistic Model setup

## Slide 9: Percentile Plots (water column)

## Slide 10: Results
FOL002

## Slide 11: Results
FOL002

## Slide 12: Results
FOL002

## Slide 13: Results
FOL002

## Slide 14: Results
FOL002

## Slide 15: Results
PGC010

## Slide 16: Results
PGC010

## Slide 17: Results
PGC010

## Slide 18: Results
PGC010

## Slide 19: Results
PGC010

## Slide 20: Percentile Plots (benthic zone)

## Slide 21: Results
FOL002

## Slide 22: Results
FOL002

## Slide 23: Results
FOL002

## Slide 24: Results
PGC010

## Slide 25: Results
PGC010

## Slide 26: Results
PGC010

## Slide 28: Partial Correlation Coefficients

## Slide 29: Results
FOL002
CN_c = runoff curve number
uslec_c = soil loss cover management factors
uslels = Universal Soil Loss Equation topographic factor
uslep = Universal Soil Loss Equation practice factor
uslek = Universal Soil Loss Equation (K) of soil erodibility
app_rate = application rate (kg/ha)
FROC1 = fraction of organic carbon on sediment in water column
FROC2 = fraction of organic carbon on sediment in benthic region
kd = dissociation constant (mL/g)
benthic_depth = depth of benthic region (m)
bf = provides additional constant flow through water body
bulk_density = bulk density of benthic region (g/mL)
anae_aq = benthic degradation half life (days)
fc = field capacity in the horizon (cm3 cm-3)
WP = wilting point in the horizon (cm3 cm-3)

## Slide 30: Results
PGC010
CN_c = runoff curve number
uslec_c = soil loss cover management factors
uslels = Universal Soil Loss Equation topographic factor
app_rate = application rate (kg/ha)
uslep = Universal Soil Loss Equation practice factor
kd = dissociation constant (mL/g)
uslek = Universal Soil Loss Equation (K) of soil erodibility
benthic_depth = depth of benthic region (m)
FROC2 = fraction of organic carbon on sediment in benthic region
FROC1 = fraction of organic carbon on suspended sediment in water column
DOC1 = concentration of dissolved organic carbon in water column (mg/L)
SUSED = suspended solids concentration in water column (mg/L)
PLMAS = concentration of biosolids in water column (mg/L)
anae_aq = benthic degradation half-life (days)
bulk_density = bulk density of benthic region (g/mL)

## Slide 31: The End
Questions?

## Slide 33: Deterministic Input Parameters

## Slide 34: Deterministic Input Parameters

## Slide 35: Deterministic Input Parameters

## Slide 36: Probabilistic Input Ranges

## Slide 37: Probabilistic Input Ranges

## Slide 38: Probabilistic Input Ranges

## Slide 39: Application Rates Computation
County | Sub-County District | Area of Sub-County (mi2) | Pop Density (people/mi2) [1] | Area of Watershed intersecting County (mi2) [2] (%) |  | Population in watershed [1]*[2]
Sacramento | Folsom | 27.61 | 73356 / 27.61 = 2656.86 | 26.21 | 47.44 | 69637
 | Rancho Cordova | 69.70 | 114151 / 69.70 = 1637.75 | 14.46 | 26.17 | 23682
 | Sacramento | 375.67 | 1097102 / 375.67 = 2920.39 | 9.64 | 17.45 | 28153
 | Sloughhouse | 123.09 | 7044 /123.09 = 57.23 | 2.44 | 4.42 | 140
Subtotal |  |  |  |  |  | 121612
El Dorado | South El Dorado | 765.83 | 105175 / 765.83 = 137.33 | 2.36 | 4.27 | 325
Subtotal |  |  |  |  |  | 325
Placer | Rocklin | 72.72 | 88195 /72.72 = 1212.80 | 0.13 | 0.24 | 158
Subtotal |  |  |  |  |  | 158
Total |  |  |  | 55.25 | 100.00 | 122095
Folsom Watershed
[8.39% * PUR(Sacramento County)] +
[0.18% * PUR(El Dorado County)] +
[0.04% * PUR(Placer County)]
County | Total Population in County [3] | Population in the watershed (from above table) [4] | Fraction (%) [4]/[3]
Sacramento | 1450277 | 121612 | 8.39
El Dorado | 181465 | 325 | 0.18
Placer | 361518 | 158 | 0.04

## Slide 40: Application Rates Computation
County | Sub-County District | Area of Sub-County (mi2) | Pop Density (people/mi2) [1] | Area of Watershed intersecting County (mi2) [2] (%) |  | Population in watershed [1]*[2]
Placer | Lincoln | 211.75 | 73015 / 211.75 = 344.82 | 23.19 | 49.46 | 7997
 | Roseville | 37.78 | 117209 / 37.78 = 3102.41 | 15.61 | 33.29 | 48429
 | Rocklin | 72.72 | 88195 / 72.72 = 1212.80 | 6.74 | 14.38 | 8175
Subtotal |  |  |  | 45.54 | 97.13 | 64601
Sutter | South Sutter | 131.96 | 2570 /131.96 = 19.48 | 1.35 | 2.88 | 27
 |  |  |  | 1.35 | 2.88 | 27
Total |  |  |  | 46.89 | 100.00 | 646280
County | Total Population in County [3] | Population in the watershed (from above table) [4] | Fraction (%) [4]/[3]
Placer | 361518 | 64601 | 17.87
Sutter | 95067 | 27 | 0.03
PGC Watershed
[17.87% * PUR(Placer County)] + [0.03% * PUR(Sutter County)]